Owner's Manual

Before using this unit, carefully read the sections entitled: "USING THE UNIT SAFELY" and "IMPORTANT NOTES" (p. 29-31; p. 3233).

These sections provide important information concerning the proper operation of the unit. Additionally. in order to feel assured that you have gained a good grasp of every feature provided by your new unit, Owner's manual shouid be read in its entirety. The manual should be saved and kept on hand as a convenient reference.

*	The "Mini Guide" on the back of the RC-20 provides a simple explanation of use. You can use it as a reminder of operational procedures.

Main Uses

Here are some ways in which the RC-20 can be used. You can use your own creativity to come up with other ways to enjoy using the RC20.

• "Sound On Sound" performance
New "sound on sound" possibilities let you combine performances not only
of guitar, but also vocals, percussion, and drum pads 		p. 10
• Create loop phrases
You can record phrases from a sampling CD or MD, and overdub guitar or vocals 		p. 12
• Switch loops while you perform live
Multiple R&B or techno phrase loops can be stored, and selected successively
while you perform (Phrase Shift) 	[	p. 20
• As a phrase trainer
Play your guitar while playing back phrases recorded from a CD or MD 	[	p. 16
Practice at a different tempo without changing the pitch 	[	p. 19
Erase the guitar solo or vocal when recording, to create "minus-one" data for
practicing (Center Cancel) 		p. 18
• As a backing device
Phrase trainer with a pedal that lets you start/stop or select phrases
(One-shot Playback) 		p. 16
• Special effects during a live performance
Reverse-playback of a recorded phrase 		p. 21

create new

and set the

• Simple and reliable loop play

The new "loop quantize" function automatically adjusts the  o/t loop end.
	This makes it easy for anyone to create looped phrases of an accurate length,

• Up to 5 minutes 30 seconds of extended phrase recording

Up to ten different loop phrases and one one-shot phrase can be saved for a total of 5
	minutel and 30 seconds of recording.

•  tim phmle tempo in real time

Tl  O •  earn be controlled in real time without affectin8 its pitch. A
	phrm N I1 IZXXlOl'y O be x#de to match the terapo of a live

mtl' I•!	to
	learn mi

|A/JX IN jack.

while it is being

Main features 	; 	2

Contents 	3
Panel Descriptions 	4
Installing batteries 	7
Making connections 	8
Tuming the power on/off 	9
Important < Caution when turning off the power > 	9

Recording a guitar or vocal performance to create s phrase loop 	10
	Recording a phrase from CD/MD to create a phrase loop 	12
	Playing/overdubbing along with a saved phrase 	16
	Using the RC-20 for practicingmPhrase Trainer 	18
	Creating minus-one data 	18
	Practicing at a different tempo 	19
	Playing back in various ways 	20
	Using the pedal to switch phrases (Phrase Shift) 	20
	Play back a phrase backward (Reverse Playback) 	21
	Playing a phrase only once (One-shot Playback) 	21
	Saving or deleting a phrase 	22
	About memory 	22
	Write Protect mode 	22
	Saving a phrase 	23
	Erasing a saved phrase (Delete) 	23
	About the tempo and time signature 	24
	Setting the tempo 	24
	Setting the time signature 	25
	What is Loop Quantize? 	25
	About the guide tone 	26
	Troubleshooting 	27
	Specifications 	28
	USING THE UNIT SAFELY 	29
	IMPORTANT NOTES 	32
	Index 	34

4

10

Front Panel

I    2	3

the number of times that is equivalent to the numerator of the desired time signature (p. 25).

WRITE Button

• This button is used to save a recorded phrase into internal memory (p. 23).

• You can use the WRITE button and EXIT button to delete the contents of the selected phrase track (p. 23).

EXIT Button

This button is used to halt a phrase save or delete operation.

8

AUTO START Button

Turn this button on (indicator lit) if you want recording to begin simultaneously when the performance begins.

9

MODE Button

This button selects the recording method.

11 10

LEVEL Knob

This knob adjusts the play volume of the

phrase.

*	This knob does not adjust the input level from the INST/MIC/AUX IN jacka or the volume of the guide tone.

2

GUIDE Knob

This knob adjusts the volume of the guide tone that sounds according to the tempo while a phrase is being recorded or played.

LOOP QUANTIZE Indicator

This indicator lights when the Loop Qktte

function (p. 25) is activated.

3

PHRASE SELECT Knob

This knob selects the phrase track that will be saved or played.

PHRASE USED Indicator

This indicator will light if a phrase has been saved in the selected track.

MEMORY FULL Indicator

The indicator will light when the remaining capacity of internal memory is getting low (p. 27). If the remaining memory runs out while a phase is being saved, this indicator will blink.

MIC Knob

This knob adjusts the input level from the MIC jack.

INST Knob

This knob adjusts the input level from the INST jack.

PEAK Indicator

This indicator will light when the level of the input is excessively high.

REVERSE Button

Turn this button on (indicator lit) when you

want the phrase to play back in reverse (p. 21).

TAP TEMPO Button

This button is used to set the tempo or time signature.

The indicator will light to indicate the current tempo and time signature (red on the first beat, green on subsequent beats).

• Tempo

Specify the tempo by the interval at which

you press the button (p. 24).

• Time signature

When you press and hold the button for two seconds or longer, it will switch to time signature setting mode. Then press the button

POWER Indicator

This indicator will light when the power is on.

*	When the batteries run down, the POWER indicator will become dim. When this occurs, please replace them with new batteries.

11

REC Indicator

This indicator will light during recording. PLAY Indicator

This indicator will light while a phrase is playing.

OVERDUB Indicator

This indicator will light during overdubbing.

12

Left Pedal

• Provides for switching among phrase recording, playback, and overdubbing.

A phrase track in which no phrase is recorded: recording --) playback -) overdubbing

A phrase track in which a phrase has been recorded: playback --) overdubbing

• If you press and hold the pedal for two seconds or longer, the unsaved phrase will be deleted.

Right Pedal

• Provides for switching among phrase

recording, playback, and overdubbing.

•	You can set the tempo to the timing at which you press the pedal.

• If you press and hold the pedal for two seconds or longer, the unsaved phrase will be deleted (clear; p.22).

Rear Panel

13 14	15	16 17 18     19
13			18
INST Jack			OUTPUT Jack

A guitar or other	instrument	can	be	Connect a guitar amp or speaker to this jack.

connected to this jack.	*If you are using batteries, the power will be
14	turned on when you insert a plug (for
MIC Jack	connection to an amp or speaker) into the this

Accepts connection of a microphone,	jack.

Used when you wish to record a vocal	or	NOTE:	Do not connect headphones to this

instrumental performanceviaamicrophone,	jack. Doing so may damage the
15	headphones.

19

AUX IN Jack
Connect to the headphones jack of a CD or	AC Adaptor Jack
MD.	Connect an AC adaptor (sold separately) to
16	this jack.

Insert the included batteries as shown in the diagram, being careful to observe the correct polarity.

PHRASE SHIFT Jack

If you wish to use a pedal to switch the phrase track, connect a pedal switch (sold separately; e.g., FS-5U) to this jack.

17

REVERSE Jack

If you wish to use a pedal to play back the

phrase in reverse, connect a pedal switch (sold separately; e.g., FS-5U) to this jack.

•	Be sure to observe the correct + (positive) and - (negative) orientation of the batteries.

•	When the batteries run down, the POWER indicator will become dim. When this occurs, please replace them with new batteries.

•	If the power is turned off while you are recording or overdubbing, all of the saved data may be lost (p. 9). We recommend that you use an AC adaptor as well, to guard against battery failure.

•	When replacing the batteries, use six AA batteries.

•	Do not mix new batteries with previously used batteries or batteries of a different type. Doing so may cause battery leakage.

•	The running time may be shorter depending on the type of batteries you use.

/	Expected battery life under continuous use:
		Carbon: 9 hours

Alkaline: 25 hours

These figures will vary depending on the actual conditions of use.

7

6

Microphone

Electric guitar

AUX IN jack : Stereo miniature phone other jacks : 1/4 inch phone

AC adaptor J (sold separately)

Pedal switch

(sold separately)

Guitar amp CD/MD player

*	To prevent malfunction andor damage to speakers or other devices, always turn down the volume, and turn off the power on all devices before making any connections.

*	If there are batteries in the unit while an AC adaptor is being used, normal operation will continue should the line voltage be interrupted (power blackout or power cord disconnection).

*	If you are using batteries, the power will be turned on when a connector plug for your amp or speaker is inserted into the OUTPUT jack.

* For details on installing the batteries, refer to "Installing batteries" (p. 7).

*	For details on pedal switches that can be connected to the PHRASE SHIFT jack and REVERSE jack, refer to p. 20, 21.

* Do not connect headphones to the OUTPUT jack. Doing so may damage the headphones.

*	Howling could be produced depending on the location of microphones relative to amp. This can be remedied by:

1.	Changing the orientation of the microphone(s).

2.	Relocating microphone(s) at a greater distance from speakers.

3.	Lowering volume levels.

*	If the amp and microphone are close together, the sound played back from the amp may be picked up by the microphone. If you record or overdub in such a state, the amp playback picked up by the microphone will also be recorded. You should separate the amp and microphone so that the playback from the amp is not picked up by the microphone.

Turning the power on/off

Once the connections have been completed, turn on power to your various devices in the order specified. By turning on devices in the wrong order, you risk causing malfunction and/or damage to speakers and other devices.

When turning the power on: Turn on the power of the amp or mixer last.

When turning the power off: Turn off the power of the amp or mixer first.

*	Always make sure to have the volume level turned down before switching on power. Even with the volume all the way down, you may still hear some sound when the power is switched on, but this is normal, and does not indicate a malfunction.

*	If you are using batteries, the indicator will become darker when the batteries run down. Please replace the batteries as soon as possible.

e power >

Before you turn off the power, make sure that the following conditions are met. All saved data may be lost If the power Is turned off inappropriately.

•	You must not be playing/recording/overdubbing a phrase

•	The WRITE indicator or EXIT indicator must not be lit

•	The PHRASE USED indicator is not blinking

If you are using batteries, the power will be turned off automatically when the connector plug to your amp or speaker is unplugged from the OUTPUT jack. Before unplugging this connector, make sure you check for the above states.

6, 7, 8

(4), 9

On the RC-20, the process of recording an additional performance

while a recorded performance plays back is called overdubbing.

The performance from an instrument or microphone connected to the INST jack or MIC jack can be recorded to create a phrase loop. This lets you enjoy new types of sound-on-sound playing that combine guitar, percussion, or drum pad performances.

...... 		 i : iit ......
		 WRITE EXIT AUTO START MODE • INST & MICII

1.	Select an empty phrase track

2.	Select the recording method

3.	Adjust the recording level

4. (Tempo setting)	--) If you are recording to a tempo

5. (Auto Start setting) -) If you wish to start recording when the performance begins

6. Start recording

7. Stop recording, and start playback

8. Start/stop overdubbing

9. Stop playback

10.(Save the phrase) --) If you wish to save the phrase

| o Turn the PHRASE SELECT knob to select an empty phrase track 110

(PHRASE USED indicator extinguished).

If there is no empty phrase track, or if the MEMORY FULL indicator is lit, no

further phrases can be recorded. You will need to erase unnecessary phrases (p. 23).

2. Press the MODE button to get the INST & MIC indicator to light.

3.	While you produce sound on your microphone or instrument, turn the MIC knob or INST knob to adjust the recording level.

Adjust the volume so that the PEAK indicator lights occasionally.

4.	Set the tempo by pressing the TAP TEMPO button or the right pedal several times in time with the tempo of the phrase you wish to record.

*	For details on setting the tempo, refer to "Setting the tempo" (p. 24).

*	If you are recording a phrase of a time signature other than 4/4, you must also set the time signature (p. 25).

5.	If you want recording to begin the moment you start playing, turn the AUTO START button on (indicator lit).

6. Press the left pedal to begin recording.

If Auto Start is on, recording will begin the moment you start playing.

If ouhav     "f'           r r in wi    in n m aureafter ou resstheleft edal.

ecified the tern o recordin will be in the moment edal.

*	If the internal memory is used up, recording or overdubbing may stop before you are finished. If this occurs, erase unnecessary phrases (p. 23), and try the operation again.

7. Press the left pedal to stop recording.

Simultaneously, the recorded phrase will begin playing.

*	Regardless of the timing at which you press the left pedal, the length of the phrase will be automatically adjusted in units of a measure, so that the loop phrase can be created correctly (Loop Quantize p. 25). This means that a certain amount of time may be required from when you press the left pedal until recording stops.

*	If you recorded an extremely short phrase, the length of the phrase will be adjusted automatically, and then recording will stop (p. 27).

8. If you wish to overdub onto the phrase, press the left pedal.

Each time you press the left pedal, the playback and overdubbing modes will alternate.

O. When you are finished with playback or overdubbing, press the right pedal.

10.Press the WRITE button, getting the indicator to start blinking. To save the data in the same phrase track, press the WRITE button once again.

If you wish to save the data to a different phrase track, press the WRITE button (so its indicator is blinking), use the PHRASE SELECT knob to select the desired save destination, then press the WRITE button once again.

*	For details on saving, refer to "Saving a phrase" (p. 23).

(4), 12

You can create a phrase loop by recording a performance from a CD or MD connected to the AUX IN jack. For example, you can record phrases from a sampling CD and overdub guitar or vocal onto it, or even record an entire song from an audio CD and use it for practicing.

WRITE EXIT	AUTO START MODE 0 INST & MIC

6, 7, 10, 11

1.	Select an empty phrase track

2.	Select the recording method

3.	Adjust the recording level

4.	(Tempo setting)

5.	(Auto Start setting)

--) If you are recording to a tempo

)	If you wish to start recording when the performance begins

6.	Start recording
7.	Stop recording, start playback
8.	(Save the phrase)	-) If you wish to keep the phrase

9.	(Select the overdubbing method) --) If you wish to change the overdubbing method
10.	Start playback
11.	Start]stop overdubbing
12.	Stop playback

Recording a phrase from CD/MD to create a phrase loop

|.	Turn the PHRASE SELECT knob to select an empty phrase track 110 (PHRASE USED indicator extinguished).

No further phrases can be recorded if there is no empty phrase track, or if the MEMORY FULL indicator is lit. In this case, you will have to erase unnecessary phrases (p. 23).

2. Press the MODE button to select the recording method.

•	NORMAL+FLAT AMP SIMULATE

Apply the Flat Amp Simulator effect to the sound being recorded.

•	CENTER CANCEL+FLAT AMP SIMULATE

Sounds localized at the center will be erased, and then the Flat Amp Simulator effect will be applied to the sound being recorded.

*	If an effect such as reverb has been applied to the sounds localized at the center, it may not be possible to erase the sound completely.

•NORMAL

The performance from the CD or MD will be recorded as is.

•	CENTER CANCEL

Sounds localized at the center (such as vocals or guitar solo) will be erased from the sound being recorded.

mulator compensates th (i.e., non-guitar)    | performance will sound correct when played through your guitar amp.

3.	While playing back the CD/MD, use the volume control of the CD/MD player to adjust the recording level.

Adjust the volume so that the PEAK indicator lights occasionally.

When you have finished adjusting the volume, stop the CD/MD player for now, and put it in playback-ready mode.

4o	Set the tempo by pressing the TAP TEMPO button or the right pedal several times in time with the tempo of the phrase you wish to record.

*	For details on setting the tempo, refer to "Setting the tempo" (p. 24).

*	If you are recording a phrase of a time signature other than 4/4, you must also specify the time signature (p. 25).

$.	If you want recording to begin the moment the performance begins, turn the AUTO START button on (indicator lit).

9°

6o Press the left pedal to begin recording.

If the AUTO START button is on, recording will begin the moment the CD/MD begins to play.

If the AUTO START button is off, recording will begin the moment you press the left pedal. Listen to the sound of the CD/MD, and press the left pedal at the appropriate time.

*	If the internal memory is used up, recording or overdubbing may stop before you are finished. If this occurs, erase unnecessary phrases (p. 23), and try the operation again.

7. Press the left pedal to stop recording.

Simultaneously, the recorded phrase will begin playing. The tempo of the phrase

will also be set automatically.

*	The automatic tempo setting is calculated with a time signature of 4/4. If you are recording a phrase whose time signature is different, you must re-specify the correct tempo after recording (p. 24).

*	If you recorded an extremely short phrase, the length of the phrase will be adjusted automatically, and then recording will stop (p. 27).

8.	Press the WRITE button, getting the indicator to start blinking. When you do so, playback will stop automatically. To save the data in the same phrase track, press the WRITE button once again.

If you wish to save the data in a different phrase track, press the WRITE button (so its indicator is blinking), use the PHRASE SELECT knob to select the desired save destination, and then press the WRITE button once again.

*	For details on saving, refer to "Saving a phrase" (p. 23).

We recommend that you save the phrase at this point. If you are not
		content with the results of subsequent overdubbing, you can then
		cancel only the overdubbing.

Press the MODE button to select how overdubbing will occur.

As you did in step 2, select the overdubbing method. If you wish to overdub a performance from guitar or mic, select INST & MIC.

| Oo Press the left pedal to begin playback.

| 1.When you wish to overdub (p. 10) along with the phrase, press the left pedal. Each time you press the left pedal, you will switch between playback and overdubbing modes.

| 2.To stop playback and overdubbing, press the right pedal.

5, 6

(4), 7

1.	Select a phrase track

2.	Select the recording method

3.	Adjust the recording level

4.	(Adjust the tempo)

5.	Start playback

6.	Start/stop overdubbing

7.	Stop playback

8.	(Save the phrase)

Playing/overdubbing along with a saved phrase

|.	Turn the PHRASE SELECT knob to select the phrase track in which the

desired phrase is saved.

2. Press the MODE button to get the INST & MIC indicator to light.

3. Turn the MIC knob or INST knob to adjust the recording level.

4. If necessary, press the TAP TEMPO button several times to set the tempo.

You can also set the tempo by pressing the right pedal instead of the TAP TEMPO

button.

*	For details on setting the tempo, refer to "Setting the tempo" (p. 24).

*	It is not possible to adjust the tempo beyond a certain limit.

5. Press the right pedal to begin playback.

6. When you wish to overdub along with the phrase, press the left pedal.

Each time you press the left pedal, you will switch between playback and

overdubbing modes.

*	If the internal memory is used up, overdubbing may stop before you arefinished. If this occurs, erase unnecessary phrases (p. 23), and try the operation again.

7. When you are finished playing or overdubblng, press the right pedal.

8.	Press the WRITE button, getting the indicator to start blinking. To save the data in the same phrase track, press the WRITE button once again.

If you wish to save the data in a different phrase track, press the WRITE button (so its indicator is blinking), use the PHRASE SELECT knob to select the desired save destination, and then press the WRITE button once again.

*	For details on saving, refer to "Saving a phrase" (p. 23).

*If you continue looping in Overdub mode, unwanted noise will also be recorded repeatedly. You should use Overdub mode only while recording a phrase.

16	17

When recording a song from CD or MD, you can erase vocals or guitar solos that locate at the center of the sound field. This function makes it easy to create "minus-one" data for practicing.

You can also adjust the tempo while the phrase plays back. Unlike a multitrack tape recorder, changing the tempo of the song will not affect the pitch. This is convenient when you wish to slow down the tempo for practicing.

Creating minus-one data

I. Turn the PHRASE SELECT knob to select an empty phrase track 110

(PHRASE USED indicator extinguished).

If there is no empty phrase track or if the MEMORY FULL indicator is lit, no further

phrases can be recorded. You will need to erase unnecessary phrases (p. 23).

2. Press the MODE button to select the recording method.

If you wish to create minus-one data, select "CENTER CANCEL" or "CENTER

CANCEL+FLAT AMP SIMULATE" (p. 13).

*	If an effect such as reverb has been applied to the sounds localized at the center, it may not be possible to erase the sound completely.

3.	Set the tempo by pressing the TAP TEMPO button or the right pedal several times in time with the tempo of the phrase you wish to record.

4.	If you want recording to begin at the moment the performance starts, turn the AUTO START button on (indicator lit).

5. Press the left pedal to start recording.

*	If the internal memory is used up, recording or overdubbing may stop before you are finished. If this occurs, erase unnecessary phrases (p. 23), and try the operation again.

6. Press the right pedal to stop recording.

When recording ends, the tempo of the phrase will be assigned automatically.

*	The automatic tempo setting is calculated with a time signature of 4/4. If you are recording a phrase whose time signature is different, you must re-set the correct tempo after recording (p.24).

7.	Press the WRITE button, getting the indicator to start blinking. To save the data in the same phrase track, press the WRITE button once again.

If you wish to save the data in a different phrase track, press the WRITE button (so its indicator is blinking), use the PHRASE SELECT knob to select the desired save destination, and then press the WRITE button once again.

*	For details on saving, refer to "'Saving a phrase" (p. 23).

Practicing at a different tempo

To change the tempo while the phrase is playing, press the TAP TEMPO

button several times at the desired interval. The tempo of the phrase will change temporarily.

*	For details on changing the tempo, refer to "Setting the tempo" (p. 24).

*	It is not possible to adjust the tempo beyond a certain limit.

If you wish to keep the modified tempo, save the phrase (p. 23).

Using the pedal to switch phrases (Phrase Shift)

While a phrase is playing, you can press a pedal switch connected to the PHRASE SHIFT jack to switch to the phrase track of the following number.

It is convenient to store the phrases in consecutive phrase tracks according to the order in which you intend to perform them.

If you prepare Intro, looped phrase, and Ending, you can use the
		Phrase Shift to play them back as a song.

1.	Connect a pedal switch such as the FS-5U (sold separately) to the PHRASE SHIFT jack (p. 8).

*	Pedal switches made by another manufacturer may operate in the opposite way. Such pedal switches cannot be used.

*	If you are using the FS-5U, move the polarity switch toward the jack.

Play back a phrase backward (Reverse Playback)

Playing a recorded phrase from the end toward the beginning is called "reverse playback." The result is similar to playing a tape in reverse.

By pressing the REVERSE button, lighting its indicator, you can use reverse playback. To return to normal playback, extinguish the indicator.

Since this can produce unexpected results, it may be useful as a gimmick during a live performance.

*	If you save a phrase with the REVERSE button turned on, the state of the button will also be memorized. If you will always want a certain phrase to play back in reverse, you should save it with the REVERSE button turned on.

*	If you overdub onto a phrase that plays back in reverse, the sound you've overdubbed is recorded as being for normal playback.

You can also control reverse playback by using the pedal switch
	instead of the REVERSE button.
	Connect a pedal switch such as the FS-5U (sold separately) to the
	REVERSE jack (p. 8).
	* Pedal switches made by some other manufacturer may operate in the
	opposite way. Such pedal switches cannot be used.
	* If you are using the FS-SU, move the polarity switch toward the jack.
	* The FS-5L cannot be used.

*	The FS-5L cannot be used.

2.	Turn the PHRASE SELECT knob to select the phrase that you wish to play first.

3.	Press the left pedal to begin playing the phrase.

4. When you want to switch phrases, press the pedal switch.

When the currently playing phrase returns to the loop start, playback will switch

to the next number phrase.

*	Even if you press the pedal several times while the same phrase is playing, only the next number phrase will be selected.

*	Once you reach number 10 when switching phrases, further presses of the pedal switch won't switch you to a different phrase.

5. Press the right pedal to stop playback.

When you start playback again, the phrase selected with the PHRASE SELECT

knob will play.

If, while a phrase is playing back, you turn the PHRASE SELECT
		knob to select the phrase track that will be played next, the next
		phrase will begin at the moment that the currently playing phrase
		returns to the loop start.

Playing a phrase only once (One-shot Playback)

The phrases saved in phrase tracks 1-10 will continue playing (looping) from the beginning to the end of the phrase until you stop them by pressing the right pedal. In contrast, the phrase saved in phrase track 11 will play back only once from the beginning to the end of the phrase, and will then stop automatically.

You can take advantage of this by using phrase track 11 to store phrases for playing dual guitar solos or sound effects in a live concert.

*	The overdubbing operation cannot be performed on phrase track 11. If you press the left pedal during playback, playback will begin once again from the beginning of the phrase. (Overdubbing can be done by copying the data to another phrase track.)

22

About memory

The memory of the RC-20 is divided into two areas: phrase tracks 1-11 and temporary memory.

Record/

Overdubbing

Save

Phrase track

A phrase that you record or overdub is first stored in temporary memory.

The phrase stored in temporary memory is temporary, and will be erased when the following operations occur. Before you perform any of these operations, make sure to save the phrase in a phrase track if you wish to keep it (p. 23).

•	When you turn off the power

•	When you select a different phrase track

•	When you begin other overdubbing before you save

If you wish to erase (clear) only the phrase in temporary memory,
		press and hold the left or right pedal for two seconds or longer.

What is a phrase track?

A phrase track is an area of internal memory in which phrases are stored. Phrases that are saved here will not be lost when the power is turned off. Also, phrases that are saved here can be selected at any time by using the PHRASE SELECT knob. The phrases that can be saved in phrase tracks 1-11 can have a maximum total length of 5 minutes 30 seconds.

Phrase tracks 1-10: contain loop phrases.

Phrase track 11:    contains a one-shot phrase.

Write Protect mode
		You can temporarily prevent phrases from being saved or erased. To

do this, press and hold the WRITE button while you turn on the
	power. This setting will be cleared when you turn off the power, so
	the next time power is turned on, you will once again be able to save
	or erase phrases.

Saving a phrase

When you have finished recording/overdubbing, or after you have edited the tempo or other settings of a phrase, you can save it.

If you turn off the power, select a different phrase track, or overdub a
		different phrase before saving a phrase, the unsaved phrase will be lost.

I.	Press the WRITE button, getting the indicator to start blinking.

The RC-20 will be ready to save.

*	To copy the data, select the copy-source phrase track, and press the WRITE button.

2. Use the PHRASE SELECT knob to select the unused or empty track.

*	It is not possible to save to a phrase track that already contains a hrase (the PHRASE USED indicator will be lit).

3. Press the WRITE button once again to save the phrase.

While the data is being saved, the indicator will light. When savmg is complete, the

indicator goes out.

*If you decide not to save, press the EXIT button. However, if you have turned the PHRASE SELECT knob to select another phrase track, the recorded phrase will be lost when you press the EXIT button, and you will switch to the selected phrase.

Never turn off the RC-20's power while the WRITE indicator or the
		EXIT indicator is lit. Doing so will cause all data saved in the phrase
		tracks to be lost.

Erasing a saved phrase (Delete)

I o Turn the PHRASE SELECT knob to select the phrase track that you wish to delete.

2.	Simultaneously press the WRITE button and the EXIT button to get both indicators to blink.

The RC-20 will be ready to delete the data.

3. Press the WRITE button and EXIT button once again to delete the data.

The indicator will be lit while the data is being deleted, and will go out when the deletion is complete.

Never turn off the RC-20's power while the WRITE indicator or the
		EXIT indicator is lit. Doing so will cause all data saved in the phrase
		tracks to be lost.

*	If you decide not to delete it, press the EXIT button.

*	It is not possible to delete all phrase tracks in one operation.

The RC-20 allows you to set the tempo and time signature separately for each phrase. These settings also determine how the guide tone will play, and how loop quantization will occur. This means that if the tempo and time signature are correctly set before recording, it will be easy to create a correct loop phrase.

*	The default time signature is 4/4. If you are recording a phrase with a 4/4 time signature, it is not necessary to set the time signature.

automatic tempo settings

In the following cases, the tempo of the phrase will be set automatically after it is recorded.

•	When you record a performance from a device connected to the AUX IN jack without setting the tempo

•	When you record a performance from an instrument or microphone connected to the INST or MIC jacks without setting the tempo

•	The automatic tempo setting is calculated with a time signature of 4/4. If you are recording a phrase whose time signature is different, you must re-set the correct tempo after recording.

About the tempo and time signature

Setting the time signature

If you are recording a phrase with a time signature of other than 4/4, set the correct time signature before recording.

*	It is not possible to change the time signature after recording.

* It is not possible to set a time signature whose denominator is anything other than 4.

| o Turn the PHRASE SELECT knob to select the phrase track you wish to record.

2o Press and hold the TAP TEMPO button for two seconds or longer.

The indicator will blink, then go out, and you will be able to set the time signature.

3.	Press the TAP TEMPO button as many times as the time signature you wish to set.

4°	When you have finished setting the time signature, the indicator will blink, and you will automatically return to the state in which you can make tempo settings.

Setting the tempo

If you are recording a performance from an instrument or microphone connected to the INST or MIC jacks, set the tempo before recording.

You can change the tempo for playing back the stored phrase.

*	If you change the playback tempo, then store the phrase, the modified tempo will be stored. If you do not save it, the tempo change will be lost.

I.	Turn the PHRASE SELECT knob to select the phrase track you wish to use. If you are recording a new phrase, select the track you wish to record.

2. Press the TAP TEMPO button several times at the desired tempo.

The tempo will be set according to the intervals at which you press the button.

*	The tempo can also be set by pressing the right pedal instead of the TAP TEMPO button. However, the right pedal cannot be used while a phrase is playing.

*	There are limits on how far the tempo can be changed.

*	If you wish to record a new phrase at the same tempo as the previously-selected phrase, press the TAP TEMPO button / right pedal once.

*	By starting recording without setting the tempo, you can create a loop phrase without using the Loop Quantize function.

It is not possible to set or change the tempo while a phrase is stored
		in temporary memory. If you are unable to set or change the tempo,
		delete (clear) the phrase stored in temporary memory, and try the
		operation again (p. 22).

What is Loop Quantize?

The timing at which you stop recording the phrase is very important in order to create an accurately looped phrase. When using devices other than the RC-20, it was necessary to become skilled at operating the pedal, through much practice.

The RC-20, however, has a new Loop Quantize function that automatically corrects the length of the phrase by referring to the information in the Tempo settings so that an accurately looped phrase can be created even if recording is stopped at a

slightly inaccurate timing.

Without LOOP QUANTIZE	LOOP QUANTIZE

Phrase	,	Phrase	,
Loop Phrase		Loop Phrase

*	Loop Quantize is valid only when you have set the tempo before recording (the LOOP QUANTIZE indicator will be lit). If you have not set the tempo here recording, or during overdubbing, the Loop Quantize function is not active (LOOP QUANTIZE indicator extinguished).

GUIDE

A guide tone will sound while you are playing or recording a phrase.

The volume of the guide tone can be adjusted with the GUIDE knob.

If you do not wish to hear the guide tone, turn the GUIDE knob to the OFF position.

If you wish to change the sound of the guide tone, hold down the EXIT button and press the TAP TEMPO button several times. Each time you press the TAP TEMPO button, the guide tone (four types) will change.

* When you save a phrase (p. 23), the currently selected guide tone will also be remembered.

The guide tone will not be heard when you record a phrase for which
	no tempo has been set. However, the tempo will be calculated
	automatically when you have finished recording, and the guide tone
	will play during playback.

Power does not turn on

•	Is an amp or speaker connected to the OUTPUT jack?

)	If you are using batteries, the power will not turn on unless an amp or speaker is connected to the OUTPUT jack. Check the connections (p. 8).

•	Have the batteries run down?

-) Install new batteries (p. 7).

•	Is the correct AC adaptor (sold separately) connected?

•	") Check the connections once again (p. 8).

No sound/not loud enough

•	Have the connections to other devices been made correctly?

-) Check the connections once again (p. 8).

•	Has the volume been turned down on the connected guitar amp or other device? -) Check the settings of the connected device.

•	Could you be using a connection cable that contains a resistor?

)	Use a connection cable that does not contain a resistor.

Recorded/overdubbed sound cannot be heard or is too quiet

-) Use the LEVEL knob to adjust the volume.

Guide tone cannot be heard/is not loud enough

)	Use the GUIDE knob to adjust the volume.

)	The guide tone will sound when:

•	you've set the tempo before recording

to an empty phrase

•	you play back a phrase

Recording/overdubbing ends prematurely

You have run out of memory. Delete unneeded phrases (p. 23), and perform the recording/overdubbing once again.

Recording does not end immediately when you press the pedal

The length of the phrase will be automatically adjusted when you record using Loop Quantize or when you record an extremely short phrase, meaning that recording may not end immediately when you press the pedal.

Recording begins immediately even though the Auto Start function is on

If there is a significant amount of noise (for example due to distortion), that noise may be enough to trigger the beginning of recording. Reduce the noise (for example by lowering the distortion level).

The MEMORY FULL indicator lights even though there should be time remaining for recording

•  In the situations listed below, temporary memory for overdubbing (p. 22) is allocated separately from the phrase. Since any calculation of available recording time must take such temporary memory into account, the MEMORY FULL indicator may light. • When a phrase is selected

• When the playback tempo is changed • When the Write operation is executed

Recorded an extremely short phrase, but the length of the phrase has changed

• -) The minimum length of time required for a loop phrase is approximately 1.5 seconds. If the phrase you've recorded is shorter than that, the length is automatically multiplied by a factor of two, four, eight, or more until it reaches an acceptable length.

26	27

USING THE UNIT SAFELY

CAUTION

symbol at left, it means that the power-cord plug m.ust be unplugged from the outlet.

Nominal Input Level

INPUT:	-20 dBu (variable)
MIC:	-40 dBu (variable)
AUX IN:	-10 dBu

Input Impedance

INPUT:	1 M f
MIC:	1 k f2
AUX IN:	47 k f2

Nominal Output Level

OUTPUT: -20 dBu

Output Impedance

lkf

Recommended Load Impedance

10 k f2 or greater

Internal Memory

Recording Time: 5 min. 30 sec. (max.)

10 loop phrases + 1 one-shot phrase (max.)

Controls

REC/PLAY/OVERDUB Pedal,

STOP/TAP TEMPO Pedal,

INST Knob, MIC Knob,

PHRASE SELECT Knob, GUIDE Knob,

LEVEL Knob, REVERSE Button,

TAP TEMPO Button, WRITE Button,

EXIT Button, AUTO START Button,

MODE Button

Indicators

POWER (serves also as battery check indicator),

REC, PLAY, OVERDUB, PEAK,

PHRASE USED, MEMORY FULL,

LOOP QUANTIZE, TAP TEMPO, REVERSE,

WRITE, EXIT, AUTO START, INST & MIC, NORMAL, CENTER CANCEL,

FLAT AMP SIMULATE

Connectors

INST Jack, MIC Jack,

AUX IN Jack (Stereo miniature phone type), PHRASE SHIFT Jack, REVERSE Jack, OUTPUT Jack

Power

DC 9V: Dry battery (AA type) x 6, AC Adaptor

Power Consumption

85 mA (9 V max.)

*	Expected battery life under continuous use: Carbon: 9 hours Alkaline: 25 hours

These figures will vary depending on the actual conditions of use.

Dimensions

173 (W) x 158 (D) x 57 (H) mm

6-13/16 (W) x 6-1/4 (D) x 2-1/4 (H) inches

Weight

1.2 kg / 2 lbs 7 oz (including batteries)

Accessories

Owner's Manual

Roland Service (Information sheet)

Dry battery (AA type) x 6

Sound Library for RC-20 (Sample Phrase CD)

Options

AC Adaptor (PSA-series)

Foot Switch (FS5U)

0 dBu = 0.775 Vrms

In the interest of product improvement, the specifications and/or appearance of this unit

are subject to change without prior notice.

[	INSTRUCTIONS FOR THE PREVENTION OF FIRE ELECTRIC SHOCK OR INJURY TO PERSONS ]

About/',WARNING and/,CAUTION Notices

Used for instructions intended

to alert the user to the risk of /WARNING death or severe injury should

the unit be used improperly.

Used for instructions intended to alert the user to the risk of injury or material damage should the unit be used improperly.

* Material damage refers to damage or other adverse effects caused with respect to the home and all its furnishings, as well to domestic animals or pets.

About fle Symbols

The/ symbol alerts the user to important instructions or warnings.

The specific meaning of the symbol is determined by the design contained within the triangle. In the case of the symbol at left, it is used for general cautions, warnings, or alerts to danger.

The Q symbol alerts the user to items that must never be carried out (are forbidden). The specific thing that must not be done is indicated b.y the desin contained within the circle. In tte case of the symbol at left, it

means that	the unit must never be
	disassembled.

The • symbol alerts the user to things that must be carried out. The specific thing that must be done is indicated by the design contained within the circle. In the case of the

FOLLOWING ...............................

•	Before using this unit, make sure
	to read the instructions below, and
	the Owner's Manual.

• Do not open (or modify in any

way) the unit or its AC adaptor.

•	Do not attempt to repair the unit, or replace parts within it (except when this manual provides specific instructions directing you to do so). Refer all servicing to your retailer, the nearest Roland Service Center, or an authorized Roland distributor, as listed on the "Information" page.

•	Never use or store the unit in  places that are:

•	Subject to temperature

extremes (e.g., direct sunlight in  an enclosed vehicle, near a heating duct, on top of heat-generating equipment); or are

•	Damp (e.g., baths, washrooms,

on wet floors); or are

•	Humid; or are

•	Exposed to rain; or are

•	Dusty; or are

•	Subject to high levels of vibration.

•	Make sure you always have the    A unit placed so it is level and sure to remain stable. Never place it on stands that could wobble, or on inclined surfaces.

[	/WARNING

•	Use only the specified AC adaptor, and make sure the line voltage at the installation matches the input voltage specified on the AC adaptor's body. Other AC adaptors may use a different polarity, or be designed for a different voltage, so their use could result in damage, malfunction, or electric shock.

•	Do not excessively twist or bend the
	power cord, nor place heavy objects
	on it. Doing so can damage the cord,
	producing severed elements and
	short circuits. Damaged cords are fire
	and shock hazards!

•	This unit, either alone or in combination with an amplifier and headphones or speakers, may be capable of producing sound levels that could cause permanent hearing oss. Do not operate for a long period of time at a high volume level, or at a level that is uncomfortable. If you experience any hearing loss or ringing in the ears, you should immediately stop using the unit, and consult an audiologist.

•	Do not allow any objects (e.g., flammable material, coins, pins); or liquids of any kind (water, soft drinks, etc.) to penetrate the unit.

[	zWARNiNG	]

•	Immediately turn the power off, remove the AC adaptor from the outlet, and request servicing by your retailer, the nearest Roland Service Center, or an authorized Roland distributor, as listed on the "Information" page when:

•The AC adaptor or the power-

supply cord has been damaged; or

•	Objects have fallen into, or liquid

has been spilled onto the unit; or

•The unit has been exposed to rain

(or otherwise has become wet); or

•	The unit does not appear to operate normally or exhibits a marked change in performance.

•	In households with small children, an adult should provide supervision until the child is capable of following all the rules essential for the safe operation of the unit.

•	Protect the unit from strong impact.
	(Do not drop it!)

•	Do not force the unit's power-supply cord to share an outlet with an unreasonable number of other devices. Be especially careful when using extension cords--the total power used by all devices you have connected to the extension cord's outlet must never exceed the power rating (watts/amperes) for the extension cord. Excessive loads can cause the insulation on the cord to heat up and eventually melt through.

•	Before using the unit in a foreign country, consult with your retailer, the nearest Roland Service Center, or an authorized Roland distributor, as listed on the "Information" page.

[	,/WARNING

•	Batteries must never be recharged, heated, taken apart, or thrown into fire or water.

[	z CAUTION	]

•	The unit and the AC adaptor
	should be located so their location
	or position does not interfere with
	their proper ventilation.

•	Always grasp only the plug or the
	body of the AC adaptor when
	plugging into, or unplugging
	from, an outlet or this unit.

•	Whenever the unit is to remain unused for an extended period of time, disconnect the AC adaptor.

•	Try to prevent cords and cables from becoming entangled. Also, all cords and cables should be placed so they are out of the reach of children.

•	Never climb on top of, nor place

heavy objects on the unit.

•	Never handle the AC adaptor body, or its plugs, with wet hands when plugging into, or unplugging from, an outlet or this unit.

•	Before moving the unit, disconnect the AC adaptor and all cords coming from external devices.

[	z CAUTION

• Before cleaning the unit, turn off

the power and unplug the AC adaptor from the outlet (p. 8).

•	Whenever you suspect the possibility of lightning in your area, disconnect the AC adaptor from the outlet.

•	If used improperly, batteries may explode or leak and cause damage or injury. In the interest of safety, please read and observe the following precautions (p. 7).

•	Carefully follow the installation instructions for batteries, and make sure you observe the correct polarity.

•	Avoid using new batteries together with used ones. In addition, avoid mixing different types of batteries.

•	Remove the batteries whenever the unit is to remain unused for an extended period of time.

•	If a battery has leaked, use a soft piece of cloth or paper towel to wipe all remnants of the discharge from the battery compartment. Then install new batteries. To avoid inflammation of the skin, make sure that none of the battery discharge gets onto your hands or skin. Exercise the utmost caution so that none of the discharge gets near your eyes. Immediately rinse the affected area with running water if any of the discharge has entered the eyes.

•	Never keep batteries together with metallic objects such as ballpoint pens, necklaces, hairpins, etc.

•	Used batteries must be disposed of in compliance with whatever regulations for their safe disposal that may be observed in the region in which you live.

In addition to the items listed under "USING THE UNIT SAFELY" on page 29-31, please read and observe the following:

Power Supply: Use of Batteries

•	Do not use this unit on the same power circuit with any device that will generate line noise (such as an electric motor or variable lighting system).

•	The AC adaptor will begin to generate heat after long hours of consecutive use. This is normal, and is not a cause for concern.

•	The use of an AC adaptor is recommended as the unit's power consumption is relatively high. Should you prefer to use batteries, please use the alkaline type.

•	Batteries should always be installed or replaced before connecting any other devices. This way, you can prevent malfunction and/or damage to speakers or other devices.

•	Batteries are supplied with the unit. The life of these batteries may be limited, however, since their primary purpose was to enable testing.

•	Before connecting this unit to other devices, turn off the power to all units. This will help prevent malfunctions and/or damage to speakers or other devices.

Placement

•	Using the unit near power amplifiers (or other equipment containing large power transformers) may induce hum. To alleviate the problem, change the orientation of this unit; or move it farther away from the source of interference.

•	This device may interfere with radio and television reception. Do not use this device in the vicinity of such receivers.

•	To avoid possible breakdown, do not use the unit in a wet area, such as an area exposed to rain or other moisture.

Maintenance

•	For everyday cleaning wipe the unit with a soft, dry cloth or one that has been slightly dampened with water. To remove stubborn dirt, use a cloth impregnated with a mild, nonabrasive detergent. Afterwards, be sure to wipe the unit thoroughly with a soft, dry cloth.

•	Never use benzine, thinners, alcohol or solvents of any kind, to avoid the possibility of discoloration and/or deformation.

Additional Precautions

•	Please be aware that the contents of memory can be irretrievably lost as a result of a malfunction, or the improper operation of the unit. To protect yourself against the risk of loosing important data, we recommend that you periodically save a backup copy of important data you have stored in the unit's memory on an MD and so on.

•	Unfortunately, it may be impossible to restore the contents of data that was stored in the unit's memory once it has been lost. Roland Corporation assumes no liability concerning such loss of data.

•	Use a reasonable amount of care when using the unit's buttons, sliders, or other controls; and when using its jacks and connectors. Rough handling can lead to malfunctions.

•	When connecting / disconnecting all cables, grasp the connector itself never pull on the cable. This way you will avoid causing shorts, or damage to the cable's internal elements.

•	To avoid disturbing your neighbors, try to keep the unit's volume at reasonable levels. You may prefer to use headphones, so you do not need to be concerned about those around you (especially when it is late at night).

•	When you need to transport the unit, package it in the box (including padding) that it came in, if possible. Otherwise, you will need to use equivalent packaging materials.

Copyright

•	Unauthorized recording, distribution, sale, lending, public performance, broadcasting, or the like, in whole or in part, pf a work (musical composition, video, broadcast, public performance, or the like) whose copyright is held by a third party is prohibited by law.

•	Do not use this unit for purposes that could infringe on a copyright held by a third party. BOSS/Roland assumes no responsibility whatsoever with regard tO any infringements of third-party copyrights arising through your use of this unit.

About the included CD

•	Use of the Sample Phrase CD "Sound Library for RC-20" supplied with this product for any purpose other than private, personal enjoyment without the permission of the copyright holder is prohibited by law. Additionally, this data must not be copied, nor used in a secondary copyrighted work without the permission of the copyright holder.

Copyright © 2001 BOSS CORPORATION

All rights reserved. No part of this publication may be reproduced in any form

without the written permission of BOSS CORPORATION.

A
AUTO START 	11, 13, 18

CENTER CANCEL 	13, 18
clear 	22

D
delete 	23

erase
	phrase track 	23
	temporary memory 	22
	F
	FLAT AMP SIMULATE 	13, 18
	Flat Amp Simulator 	13

guide tone 	26
Loop Quantize 	11, 25

minimum length of recording time o 27 minus-one data ................................ 18

O
One-shot Playback 	21
overdubbing 	10-11, 14

Phrase Shift 	20
phrase track 	22
Phrase Trainer 	18
playback 	11, 14, 17

R
recording
connected to the AUX IN jack 	12

connected to the INST/MIC jack . 10, 12 Reverse Playback ............................. 21

signature 	25
T
tempo 	24
setting 	24
tempo change 	19
temporary memory 	22

Write Protect mode 	22

I C		This product complies with the requirements of European Directive 89/336/EEC.	For EU CountHII

FEDERAL COMMUNICATIONS COMMISSION

RADIO FREQUENCY INTERFERENCE STATEMENT

This equipment has been tested and found to comply with the Ilmlt for a Clell B digital device, pufu•nt to Part 15 of the FCC Rules. These limits are designed to provide reasonable protection against hlmltul Inteffeteflce If1 • reeld•ntl•l installation. This equipment generates, uses, and can radiate radio frequsnj an•rgy •nd, If not InltallKI and used In accordance with the instructions, may cause harmful Irtterfarance to re, dlo ¢ommunlcettonl, However, thlrl Ii rio guarentae that interference will not occur in a particular Installation, If this equipment does cause h•n1ul IntarMrance to radio or television reception, which cen be determined by turning the equipment off end on, thl uler Ii anoour=ged to try to oormct the

intederence by one or more of the following measures:

Reorient or relocate the receiving antenna.

Increase the separation between the equipment end receiver,

- Connect the equipment into an outlet on a cimuit different from that to which the receiver I| onnectad,

- Consult the dealer or an experienced radlo/TV technician for help.

This device complies with Part 15 of the FCC Rules. Operation is subject to the following two ¢ondltionl:

(1) This device may not cause harmful interference, end

(2) This device must accept any interference received, including interference that may ceuM glxlellred Operation.

Unauthorized changes or modification to this system can void the users authority to operate this equipment,

This equipment requires shielded interface cables in order to meet FCC clm B Limit,

This Class B digital appraffil meeto all mClUirenlta of the CInllln Inffrno-ulng Equipment Regulations.

AVIS

Cot eLoParall num6dque de la lasse B rasdecte routes los exlgences du Rgtement sur le matdriel brouilleur du Canada.